## Slide 1: Cache Coherency Lecture
Snooping Protocol

## Slide 2: Small-Scale—Shared Memory
Caches serve to:
  Increase bandwidth versus bus/memory
  Reduce latency of access
  Valuable for both private data and shared data
What about cache consistency?

## Slide 3: What Does Coherency Mean?
Informally:
  “Any read must return the most recent write”
  Too strict and too difficult to implement
Better:
  “Any write must eventually be seen by a read”
  All writes are seen in proper order (“serialization”)
Two rules to ensure this:
  “If P writes x and P1 reads it, P’s write will be seen by P1 if the read and write are sufficiently far apart”
  Writes to a single location are serialized: seen in one order
    Latest write will be seen
    Otherwise could see writes in illogical order (could see older value after a newer value)

## Slide 4: Potential HW Coherency Solutions
Snooping Solution (Snoopy Bus):
  Send all requests for data to all processors
  Processors snoop to see if they have a copy and respond accordingly
  Requires broadcast, since caching information is at processors
  Works well with bus (natural broadcast medium)
  Dominates for small scale machines (most of the market)
Directory-Based Schemes (discuss later)
  Keep track of what is being shared in 1 centralized place (logically)
  Distributed memory => distributed directory for scalability (avoids bottlenecks)
  Send point-to-point requests to processors via network
  Scales better than Snooping
  Actually existed BEFORE Snooping-based schemes

## Slide 5: Basic Snoopy Protocols
Write Invalidate Protocol:
  Multiple readers, single writer
  Write to shared data: an invalidate is sent to all caches which snoop and invalidate any copies
  Read Miss:
    Write-through: memory is always up-to-date
    Write-back: snoop in caches to find most recent copy
Write Broadcast Protocol (typically write through):
  Write to shared data: broadcast on bus, processors snoop, and update any copies
  Read miss: memory is always up-to-date
Write serialization: bus serializes requests!
  Bus is single point of arbitration

## Slide 6: Basic Snoopy Protocols
Write Invalidate versus Broadcast:
  Invalidate requires one transaction per write-run
  Invalidate uses spatial locality: one transaction per block
  Broadcast has lower latency between write and read

## Slide 7: Snooping Cache Variations
Berkeley Protocol
Owned Exclusive
Owned Shared
Shared
Invalid
Basic Protocol
Exclusive
Shared
Invalid
Illinois Protocol
Private Dirty
Private Clean
Shared
Invalid
Owner can update via bus invalidate operation
Owner must write back when replaced in cache
If read sourced from memory, then Private Clean
if read sourced from other cache, then Shared
Can write in cache if held private clean or dirty
MESI Protocol
Modfied (private,!=Memory)
eXclusive (private,=Memory)
Shared (shared,=Memory)
Invalid

## Slide 8: An Example Snoopy Protocol
Invalidation protocol, write-back cache
Each block of memory is in one state:
  Clean in all caches and up-to-date in memory (Shared)
  OR Dirty in exactly one cache (Exclusive)
  OR Not in any caches
Each cache block is in one state (track these):
  Shared : block can be read
  OR Exclusive : cache has only copy, its writeable, and dirty
  OR Invalid : block contains no data
Read misses: cause all caches to snoop bus
Writes to clean line are treated as misses

## Slide 9: Snoopy-Cache State Machine-I
State machine for CPU requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
CPU Read hit
Place read miss
on bus
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 10: Snoopy-Cache State Machine-II
State machine for bus requests for each cache block
Appendix E? gives details of bus requests
Invalid
Shared
(read/only)
Exclusive
(read/write)
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write miss for this block
Write Back
Block; (abort
memory access)

## Slide 11: Snoopy-Cache State Machine-III
Place read miss
on bus
State machine for CPU requests for each cache block and for bus requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
CPU Read hit
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Write miss for this block
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write Back
Block; (abort
memory access)
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 12: Example
Assumes A1 and A2 map to same cache block,
initial cache state is invalid

## Slide 13: Example
Assumes A1 and A2 map to same cache block

## Slide 14: Example
Assumes A1 and A2 map to same cache block

## Slide 15: Example
Assumes A1 and A2 map to same cache block

## Slide 16: Example
Assumes A1 and A2 map to same cache block

## Slide 17: Example
Assumes A1 and A2 map to same cache block,
but A1 != A2
Notes: Why write miss first?
Because in general, only write a piece of block, may need to read it first so that can have a full vblock; therefore, need to get
Write back is low priority event.

## Slide 18: Implementation Complications
Write Races:
  Cannot update cache until bus is obtained
    Otherwise, another processor may get bus first, and then write the same cache block!
  Two step process:
    Arbitrate for bus
    Place miss on bus and complete operation
  If miss occurs to block while waiting for bus, handle miss (invalidate may be needed) and then restart.
  Split transaction bus:
    Bus transaction is not atomic: can have multiple outstanding transactions for a block
    Multiple misses can interleave, allowing two caches to grab block in the Exclusive state
    Must track and prevent multiple misses for one block
Must support interventions and invalidations

## Slide 19: Implementing Snooping Caches
Multiple processors must be on bus, access to both addresses and data
Add a few new commands to perform coherency, in addition to read and write
Processors continuously snoop on address bus
  If address matches tag, either invalidate or update
Since every bus transaction checks cache tags, could interfere with CPU just to check:
  solution 1: duplicate set of tags for L1 caches just to allow checks in parallel with CPU
  solution 2: L2 cache already duplicate, provided L2 obeys inclusion with L1 cache
    block size, associativity of L2 affects L1

## Slide 20: Implementing Snooping Caches
Bus serializes writes, getting bus ensures no one else can perform memory operation
On a miss in a write back cache, may have the desired copy and its dirty, so must reply
Add extra state bit to cache to determine shared or not
Add 4th state (MESI)